## Slide 1: Predicting Shear Fracture Growth in Sandstone
Harsh Vora
11/16/2018

## Slide 2: ML predicts failure in stick-slip experiments
Rouet-Leduc et al., 2017:
Variance of AE energy shows strongest correlation
AI can be used to predict time to failure
Notes: But
1. they used it on pre-fractured rock and failure is a function of friction.
2. They only use knowledge of fracture energy

## Slide 3: Precursory Signatures (Lei et al., 2006)
Granite
schist
Prior to failure:
Increase in Energy Release Rate
Decline in b-values
Decline in D-values
Notes: Identify various precursors
But do not build a predictive tool

## Slide 4: Objectives
“Each parameter is a function of the temporal distance to the critical point”
“An integrated analysis of two or more parameters may lead to more effective means of predicting time of the critical point”
Quantify temporal signatures of deformation in granular rock
Can they be combined to build a predictive tool?

## Slide 5: Experiments using Discrete Element Method
Induced Bonds can fail in different modes:
Tensile
Shear
Rotation
σpre

## Slide 6: Biaxial Experiments on Berea Sandstone
Parameter | Modeled | Experimental
UCS (MPa) | 85.05 | 95.00
Young’s Modulus (Pa) | 4.28 | 7.50
MC Cohesion (Pa) | 29.35 | 26.10
MC Slope | 0.55 | 0.49
3 .8 cm

## Slide 7: Method 1: Microcrack Growth
3 .8 cm

## Slide 8: Results 1: Microcrack Growth
Potential precursors to failure:
Increase in Microcracking Rate prior to failure
Peak Shear microcracking prior to failure

## Slide 9: Results 1: Microcrack Growth
Potential precursors to failure:
Increase in Microcracking Rate prior to failure
Peak Shear microcracking prior to failure

## Slide 10: Methods 2: Fracture Energy
Elastic Energy Released during fracture growth
Ef = Energy of micro-fracture (J)
Cf = Young’s Modulus (Pa)
σcf = Peak strength at microfracture genesis (Pa)
νf = volume of microfracture (m3)

## Slide 11: Results 2: Fracture Energy
Potential Fracture Energy precursors to failure:
High Variance in energy
Steep Decline in Kurtosis
Statistical Analysis:
Variance: Expectation of deviation from Mean
3. Kurtosis: Expectation of how outlier-prone a distribution is (similar to skewness)

## Slide 12: Results 2: Fracture Energy
Potential Fracture Energy precursors to failure:
High Variance
Decline in Kurtosis

## Slide 13: Methods 3: Moment Magnitude
AE events follow power law frequency-magnitude relationship
N= number of earthquakes greater than magnitude M
b = slope of frequency magnitude relationship
Spatial and Temporal clustering of Microcracks

## Slide 14: Results 3: b-value
Potential Moment precursors to failure:
Decline in b-values prior to failure
Increase in range of seismic moments

## Slide 15: Results 3: b-value
Potential Moment precursors to failure:
Decline in b-values prior to failure
Increase in range of seismic moments

## Slide 16: Why does b-value change?
1
2
3
4
6
5
7
1
2
3
4
6
5
7
Potential Moment precursors to failure:
Decline in b-values prior to failure
Increase in range of seismic moments

## Slide 17: Methods 4: Fractal Dimension
1
2
3
4
6
5
7
Correlation Integral
D is the fractal dimension,
N is the number of microcrack pairs
R is the radius
High D-value: Distributed Damage
Low D-value: Localized Damage
1
3
5
7

## Slide 18: Results 4: D-value
1
2
3
4
6
5
7
Potential Damage precursors to failure:
Decline in Fractal Dimension

## Slide 19: Summary of Precursory Signatures
Microcracking Activity:
  High Rate
  High Shear microcracking
Energy
  High Variance
Moment:
  Low b-values
  Increase in moment range
Decline in D-values

## Slide 20: Predicting Rock Failure using Neural Networks
7 Inputs:
Microcracking Rate
Microcracking Shear Fraction
Variance of Fracture Energy
b-value
Moment Range
D-value
Confining Pressure on Rock
Outputs:
Axial Stress to Failure
Axial Strain to Failure

## Slide 21: Predicting Rock Failure using Neural Networks
Inputs from 0 to 50 MPa:
Microcracking
Energy
Moment
Fractal Dimension
Axial Stress to Failure
Axial Strain to Failure
Input dataset: [91 (samples) x10 (experiments)] x 7 (parameters)
  [910 x 7]
Training: 70% of Dataset
Testing: 30% of dataset

## Slide 22: ML Result 1: Predicting Axial Stress to Failure
Targets
Training Predictions
Testing Predictions

## Slide 23: Blind Test: 25 MPa Experiment
Pre-failure
Post-failure

## Slide 24: ML Result 3: Predicting Axial Strain to Failure
Targets
Training Predictions
Testing Predictions

## Slide 25: Blind Test: 25 MPa Experiment
Pre-failure
Post-failure

## Slide 26: Summary
Identified statistical precursory signatures of deformation using:
  Microcrack Growth (Rate of Microcracking)
  Fracture Energy (Variance of Energy)
  Moment magnitude (b-value and Moment Range)
  Spatial Distribution of Microcracks (D-value)
Applied Neural Networks on precursory signatures to predict
  Axial Stress to Failure
  Axial Strain to Failure

## Slide 27: Future Work
Optimize Neural Network Architecture
  Add more features?
  Investigate biases and weights
  Hidden Layers and Number of Neurons
Improve Neural Network Predictions